## Slide 1: Physics: Chapter 1
Lesson 6: Experimental Error

## Slide 2: The Right Value
In experiments, we are trying to make measurements of actual physical phenomena.
We would like our measurements of these phenomena to actually represent the real value.
  For example if it takes exactly 3.000025 seconds for a particle to travel a certain distance, we would like to be able to make a measurement that tells us that it took exactly 3.000025 seconds!
Our ability to actually measure those phenomena is often compromised by experimental error.
One often used analogy is that of an archer. The archer would like to hit the centre of the target each time they shoot, but due to many factors, it is difficult to do so. The reason they may miss the target is due to error.
x
x
x
x
x
x
x
x
x
x
x

## Slide 3: Random vs Systematic Error
There are two general types of Experimental Error.
Random Error, is by nature…. random!
  Random errors are chance variations in the measurements. There is an equal possibility that the measurement is too big or too small. Often you have little direct control over random error, and it is by nature unpredictable.
  Random Error can come from reaction time in using a stopwatch, or small environmental changes like vibrations coming through the ground.
  Random Error can be compensated for by taking many readings and averaging them out.
Systematic Error is error that enters into an experiment usually through design issues.
  Random error is always going to offset your data by the same amount in the same direction.
  Systematic error might come from calibration issues with your equipment (eg your stopwatch doesn’t measure exactly 1.0 second every second, or your ruler is too short)
  You cannot remove systematic error from your data by averaging it out.

## Slide 4: Accuracy and Precision
Accuracy is how close a measurement is to the correct or accepted value.
Precision is how reproducible a measurement is.
Systematic Error reduces your accuracy.
Random Error reduces your precision.
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
Accurate and precise
Precise but not accurate
Accurate not precise

## Slide 5: Random Error and Systematic Error
We can tell the quality of our data by looking at a graph of it.
If there is a lot of random error, the data points will scatter a lot around the line of best fit.
If there is considerable systematic error, there will be a y-intercept when the data is supposed to go through the origin.
Random error, but low systematic error
Systematic error, but low random error.

## Slide 6: Error vs Accuracy.
Although it is possible to tell if you have random error from your data, you can never actually tell if your data is accurate.
The only way to tell if your data is accurate is if you are trying to measure a “known” quantity.